## Slide 1: Autonomous Survey Boat
Mapping shallow coastal waters we've never mapped before — depth, water quality, and real data, one autonomous mission at a time.

## Slide 2: The Problem
Greece has huge amounts of coastline and thousands of small harbors, coves, and lakes with no modern depth map or water-quality baseline
Professional survey boats + crews are expensive — nobody sends them to a small bay or lake
Result: navigation hazards go unmapped, pollution/algae bloom risk goes unmonitored, coastal changes go untracked
This data matters for boaters, fisheries, environmental monitoring, and coastal engineering — and it's simply missing for most small water bodies

## Slide 3: The Idea
Build an autonomous surface vehicle (ASV) — a small self-driving boat
It drives a survey pattern over water completely on its own
While moving, it continuously logs:
  Bottom depth (bathymetry) via downward sonar — like a fish finder
  Water quality: temperature, pH, turbidity, dissolved oxygen
  Exact GPS position for every single reading
Result: a real, publishable map of a previously unsurveyed place

## Slide 4: Why a Boat, Not a Submarine (Yet)
Underwater, you lose almost everything that makes robotics tractable:
  No GPS underwater — radio doesn't travel through water
  No WiFi/radio communication beyond a few centimeters
  Real pressure-hull engineering and active buoyancy control needed
A surface vehicle keeps GPS and radio the ENTIRE mission
A downward sonar still maps the sea floor beneath it — exactly how real hydrographic survey boats work
We get the real goal (seafloor + water data) without the two hardest problems in underwater robotics
Full submersible version: a realistic phase 2, after this works

## Slide 5: How It Works — System Overview
Hull: catamaran (twin pontoons) — stable, well-documented hobbyist design
Propulsion: twin brushless motors + marine props, one per pontoon — steer by running one side faster (differential steering)
Brain: ArduPilot "Rover" firmware on a Pixhawk-class autopilot board — open-source, proven, built exactly for GPS-waypoint autonomous vehicles
Comms: long-range telemetry radio to a laptop on shore — ordinary radio works the whole mission, no underwater acoustic modem needed
We integrate proven, open-source building blocks — our job is engineering integration, not inventing autopilot theory from scratch

## Slide 6: Sensors — Every Kind That Gives Useful Data
Core (MVP):
  GPS + compass/IMU — position and heading for every sample
  Downward sonar — bathymetry, the core "fish finder" capability
  Temperature, turbidity, pH probes — pollution and water condition indicators
  Dissolved oxygen — ecosystem health (fish kills, algae bloom risk)
Stretch goals once MVP works:
  Conductivity/salinity, downward camera, lowered underwater camera pod on a winch — a genuine underwater element without full submersion risk

## Slide 7: Team Structure — 13 People, 5 Sub-Teams
Hull / Mechanical (3) — hull build, sensor mounting, waterproofing, winch mechanism
Propulsion & Power Electronics (2) — motors, ESCs, battery, power budget
Embedded / Autopilot Integration (3) — ArduPilot setup, GPS/telemetry, waypoint missions, safety features
Sensing (2) — sonar + water quality probe integration, calibration, GPS-tagged logging
Backend / Dashboard / Mapping (3) — live telemetry dashboard, post-mission map generation
Interface contracts between teams, weekly sync, bi-weekly demo keep 5 sub-teams working in parallel

## Slide 8: 6-Month Roadmap
Month 1 — Parts ordered, ArduPilot flashed, bench-tested manual motor control
Month 2 — First in-water test (manual control), GPS + telemetry link live
Month 3 — Sonar + water quality sensors integrated and logging
Month 4 — Full autonomy: boat drives a survey grid unattended
Month 5 — Real field survey of an unmapped local site — our actual dataset
Month 6 — Published map, write-up, demo, poster, final presentation

## Slide 9: Honest Scope — What We're NOT Promising
Full submersion / true autonomous underwater vehicle (AUV)
Underwater acoustic communication
Open ocean or rough-sea operation — calm, shallow, sheltered water only
Multi-vehicle swarm operation — this is a single-vehicle project
These are legitimate phase-2 ideas if we want to keep going after 6 months — but promising them now would overcommit us

## Slide 10: Why This Project
Covers every ECE discipline: mechanical/hull, power electronics, embedded/control systems, sensing, backend/software, data visualization
Produces a REAL dataset of a REAL place — not just a demo, an actual open dataset we can publish
Strong, honest engineering story for our CVs: "integrated an open-source autopilot stack with custom sensing across a full autonomous survey mission"
Achievable in 6 months because we integrate proven building blocks (ArduPilot Rover) rather than inventing autopilot theory from scratch
Clear, honest scope — we know exactly what we're building and what's future work

## Slide 11: Next Steps
Confirm the 5 sub-teams and assign a Technical Lead per team
Lock the budget and funding approach (shared fund vs. department/sponsor grant)
Finalize hull dimensions and order the first parts: autopilot board, GPS, motors/ESCs, battery
Set up the repo, project board, and interface contracts for the 5 sub-teams
Target: manual-controlled first water test by end of Month 2